## Slide 1
TraceMate
Guided diagnostics and trace export for vehicle testing
A focused Android workflow that connects the technician to the head unit and a headless CAPTURE_TOOL_PLACEHOLDER Mac.
AUTOMATE
Connection readiness, firewall preparation, ADB validation, and repeatable CAPTURE_TOOL_PLACEHOLDER control.
SIMPLIFY
Select and export head-unit traces to a USB stick through one visible, guided flow.
PROTECT
Explicit user actions, observable progress, retries, and recovery for long-running transfers.
PROJECT OVERVIEW
Android app | Head unit diagnostics | CAPTURE_TOOL_PLACEHOLDER capture bridge
TRACEMATE / TECHNICAL OVERVIEW
Shareable overview

## Slide 2
02
System topology
Two independent network paths keep vehicle diagnostics and CAPTURE_TOOL_PLACEHOLDER control deliberate and traceable.
HEAD UNIT
SSH + ADB WLAN hotspot USB host
ANDROID APP
TraceMate Workflow controller Visible status
MAC MINI
Headless CAPTURE_TOOL_PLACEHOLDER agent SSH / SCP endpoint CAPTURE_TOOL_PLACEHOLDER captures
MOBILE_DEVICE_PLACEHOLDER
USB-connected to Mac CAPTURE_SESSION_PLACEHOLDER target
USB STICK
Physically connected to head unit
WLAN hotspot | SSH + ADB
Android Ethernet tethering | SSH + SCP
USB
Local copy
Store-and-forward: the Mac has no direct head-unit route. Android retrieves completed CAPTURE_TOOL_PLACEHOLDER captures, then uploads them to the head-unit USB.
TRACEMATE / TECHNICAL OVERVIEW
Shareable overview

## Slide 3
03
Automated testing and export workflows
The app exposes the current readiness and next safe action instead of requiring technicians to coordinate individual tools.
1 HEAD-UNIT READINESS
Connect to the head-unit WLAN via QR-guided setup. Automatically validate: SSH -> scoped firewall -> ADB TCP -> ADB handshake -> shell access. Display E-Release only when the connection path is ready.
2 CAPTURE_TOOL_PLACEHOLDER CAPTURE
Reach the headless Mac over Android Ethernet tethering. Guide required manual steps: MobileDevicePlaceholder trust, Bluetooth state, and CAPTURE_SESSION_PLACEHOLDER confirmation. The Mac agent owns the CAPTURE_TOOL_PLACEHOLDER process and persists capture-job state.
3 USB EXPORT
Discover traces and writable USB storage on the head unit. Select archives, show progress, allow cancellation, and report success, partial failure, or recovery. Export CAPTURE_TOOL_PLACEHOLDER captures through Android store-and-forward when required.
Technician value: fewer tool switches, fewer manual command sequences, and a repeatable handover of diagnostic artifacts.
TRACEMATE / TECHNICAL OVERVIEW
Shareable overview

## Slide 4
04
Operational reliability by design
Automation is constrained to known workflows, with visible state and recovery for field use.
Scoped firewall rules limit ADB access to the head-unit WLAN client range.
All state-changing actions require an explicit technician trigger and show progress or failure feedback.
USB exports use staged partial files and atomic rename to avoid presenting incomplete archives as final output.
Long-running exports continue in a foreground service and can reattach to a remote worker after app restart.
The headless Mac agent allows one managed CAPTURE_TOOL_PLACEHOLDER job, preserves job state, and keeps its RPC interface loopback-only.
PRIMARY OUTCOME
Reduce time from vehicle connection to usable trace package.
SECONDARY OUTCOME
Make failures actionable before a technician leaves the vehicle.
CURRENT SCOPE
Guided workflow and diagnostics; not yet a one-click production process.
TraceMate makes complex, multi-device testing easier to operate without hiding the safety-critical steps.
TRACEMATE / TECHNICAL OVERVIEW
Shareable overview